## Slide 1: How continuous temperature monitoring has aided cold chain management
The National Vaccines and Immunization (NVIP), kenya
The 15th technet conference from 16th to 20th in cascais, portugal

## Slide 2: Brief background on NVIP
Roles:
Policy regulation and oversight
Commodity security & quality assurance
Monitoring and evaluation
Advocacy and Resource Mobilization
Capacity strengthening
Conduct of appropriate operational research

## Slide 3: Program Goal
The Goal of the National Vaccines and Immunization Program is:
To ensure potent vaccines and supplies are available at SDPs when needed to serve the clients
To this end, NVIP and partners have put great efforts in working towards achieving this goal through developing and implementing strategies to strengthen the immunization supply chain at all levels of the healthcare service delivery
Long term and medium term interventions
High and low financial investment
Notes: Ensuring consistent quality product availability is key to the success of the program
12 antigens currently offered routinely; BCG, OPV, IPV, DTP-HEPB-HIB combination, PCV, ROTA, Measles Rubella, YF and TT (WCBA)

## Slide 4: Immunization Supply chain
1 Central Vaccine Store
9 Regional Vaccine stores
47 Counties (administrative only; no stores)
292 Sub-county Vaccine stores
Approximately 6,700 Immunizing HFs
Approximately 20,000 HR
Over 10,000 ( Refrigeration equipment) and 30,000 passive CCE
Standby generators
Temperature monitoring devices; 30DTRs, RTMs, CTMs
Documentation tools
Monitoring tools
etc

## Slide 5: Success story
Continuous temperature monitoring
Prior to 2013 EVM assessment, thermometers in use. No 30DTRs
IP recommended continuous temperature monitoring
Introduction of 30DTRs
  Successful introduction of FT2 in all immunizing facilities (>6000) and 9 Regional vaccine stores
  Staff from Immunizing HFs trained on how to read and record temperature and respond to ALARMs
  A new monthly temperature monitoring chart was developed in line with the indicators being monitored i.e. AM/PM temperature, heat/freeze alarms recorded
  1 year assessment was conducted to ensure proper utilisation. Experiences identified, OJT
Installation of central temperature monitoring systems in all cold rooms and freezer rooms at the Central and Regional Vaccine stores – with auto-dialer ( sends sms alerts)
Development and dissemination of cold chain maintenance SOPs – ongoing (poster)
Notes: Strategies
Assessment of the immunization supply chain, EVM assessment, Temperature monitoring study, Temperature mapping of cold rooms and freezer rooms, Feasibility study, Identifying the problem, Root cause analysis, Finding possible solutions, Resource mobilization, No cost/low cost and High cost, Prioritizing, Impact, Time, Cost and HR requirements, Implementation, EVM Improvement Plan? Monitoring and evaluation, Review and reprogramming

## Slide 6: Success story
Capacity strengthening of core staff on cold chain management
  Training of HF staff:
    EPI Operation level management training: National and county specific
    EPI microplanning: ongoing
    Mentorship program for all HWs from immunizing facilities initiated by Nairobi county
  Training of Medical engineering technicians on equipment management:
    100 trained
    WhatsApp group formed to share experiences and for consultation on CC issues
  Training of University of Nairobi student doctors and nurses on EVM
Remote temperature monitoring study using CT5 – a 1 year mini project
  Month 1 to 3 – baseline data collected
  Training of staff on the use of data for decision making
Cold chain management components integrated in Chanjo (see dashboard)
Data quality assessment and support supervision
Joint data review meetings
Notes: HWs as they collect vaccines taught how vaccine and cc management

## Slide 7: challenges
Competing priorities
Industrial action by some core staff; disruption of services and CC monitoring
High staff turn-over ; private and county HFs
Inadequate skills in responding to cold chain problems
Poor documentation
Spare parts management; currently stored at CVS affecting response time
Hard to reach areas; both rural and urban
Transport challenges
Inconsistent reporting
Inadequate no. of staff; long time to complete supervision
Use of obsolete CCE to store vaccines

## Slide 8: opportunities
Training of Sub-county managers on SOPs and contingency planning
Refresher training for HWs on 30DTRs and RTMs
Building on the cold chain component in Chanjo; Kenya’s eLMIS system
Restructuring of monthly facility in-charges meetings to discuss cold chain data and planning
Procurement of Grade A freeze protection cold chain equipment
Remote temperature monitoring study using Nexleaf CT5 – a 1 year mini project through ELMA
VAN implementation in specific counties with plans for expansion countrywide
Temperature monitoring and mapping studies
EVM assessment and Improvement Plan

## Slide 9: Lessons learnt
Having new cold chain equipment does not necessarily mean all CC problems are over. New refrigerators fail too!
With introduction of new CC technology, capacity building for healthcare staff is crucial
All healthcare staff in HFs should be updated on EPI; Mentorship, OJT and Job-aids
Feedback to the HFs is key; improves work morale and practices
Change is a continuous process and should be nurtured
Recognition for good performance promotes continuous improvement
Teamwork will achieve better results
Data review meetings encourages staff to improve documentation
Self assessments leads to personal development
Technology is not always the solution, it may be part of the problem
Right people require the right data at the right time for timely response!!!!

## Slide 10: Asanteni! Thank you!